## Slide 1: Data Link Layer Design Issues
Provides service interface to network layer.

## Slide 2: Data Link Layer Design Issues
Handles transmission errors (checksums).

## Slide 3: Data Link Layer Design Issues
Regulates data flow (flow control).

## Slide 4: Data Link Layer Design Issues
Encapsulates packets into frames (header, payload, trailer).

## Slide 5: Data Link Layer Services
**Unacknowledged Connectionless:** Sends independent frames without acknowledgement (e.g., Ethernet).

## Slide 6: Data Link Layer Services
**Acknowledged Connectionless:** Each frame individually acknowledged (e.g., 802.11).

## Slide 7: Data Link Layer Services
**Connection-Oriented:** Establishes a connection, numbers frames, guarantees delivery, order, and no duplicates.

## Slide 8: Framing Methods
**Byte Count:** Header specifies frame size (prone to errors).

## Slide 9: Framing Methods
**Flag Bytes with Byte Stuffing:** Frames start/end with flag bytes; escape byte added before flag bytes in data.

## Slide 10: Framing Methods
**Flag Bits with Bit Stuffing:** Frames start/end with flag bits; 0 inserted after five consecutive 1s in data.

## Slide 11: Framing Methods
**Physical Layer Coding Violations:** Uses encoding redundancy to delimit frames.

## Slide 12: Error Control
Receivers send acknowledgements (ACKs) or negative acknowledgements (NAKs).

## Slide 13: Error Control
Timers detect lost frames (retransmission).

## Slide 14: Error Control
Sequence numbers prevent duplicate frames.

## Slide 15: Flow Control
**Stop-and-Wait:** Sender waits for ACK before sending next frame (simple, slow).

## Slide 16: Flow Control
**Sliding Window:** Sender sends multiple frames before waiting for ACKs (efficient, complex).

## Slide 17: ARQ Techniques
**Stop-and-Wait ARQ:** One frame at a time.

## Slide 18: ARQ Techniques
**Go-Back-N ARQ:** Sender window size N; retransmits entire window on error.

## Slide 19: ARQ Techniques
**Selective Repeat ARQ:** Sender and receiver window size N; only retransmits lost frames.

## Slide 20: Piggybacking
Combines data and acknowledgements in one frame to improve efficiency.

## Slide 21: HDLC
Bit-oriented protocol.

## Slide 22: HDLC
Three station types: Primary, Secondary, Combined.

## Slide 23: HDLC
Three frame types: Information (I), Supervisory (S), Unnumbered (U).

## Slide 24: HDLC
Modes: Normal Response Mode (NRM), Asynchronous Balanced Mode (ABM).

## Slide 25: PPP (Point-to-Point Protocol)
Character-oriented, used for point-to-point connections.

## Slide 26: PPP (Point-to-Point Protocol)
Handles error detection, supports multiple protocols.

## Slide 27: PPP (Point-to-Point Protocol)
LCP (Link Control Protocol) manages link establishment and configuration.

## Slide 28: PPP (Point-to-Point Protocol)
NCP (Network Control Protocol) configures network layer protocols (e.g., IP).

## Slide 29: MAC Sublayer (IEEE 802)
Handles media access control.

## Slide 30: MAC Sublayer (IEEE 802)
Standards: 802.3 (Ethernet), 802.4 (Token Bus), 802.5 (Token Ring).

## Slide 31: Ethernet (IEEE 802.3)
CSMA/CD (Carrier Sense Multiple Access/Collision Detection).

## Slide 32: Ethernet (IEEE 802.3)
Frame format: Preamble, Destination Address, Source Address, Type, Data, Pad, Checksum.

## Slide 33: Ethernet (IEEE 802.3)
Addressing: Unicast, Multicast, Broadcast.

## Slide 34: Ethernet (IEEE 802.3)
Types: 10Base5, 10Base2, 10BaseT, 10BaseF.

## Slide 35: Token Bus (IEEE 802.4)
Token passing on a bus topology.

## Slide 36: Token Bus (IEEE 802.4)
Logical ring of stations; only token holder transmits.

## Slide 37: Token Ring (IEEE 802.5)
Token passing on a ring topology.

## Slide 38: Token Ring (IEEE 802.5)
Stations pass token; only token holder transmits.

## Slide 39: Bridges
Connect multiple LANs.

## Slide 40: Bridges
Types: Transparent, Source Route, Spanning Tree, Remote.

## Slide 41: Bridges
Learning, Flooding, Filtering, Forwarding, Aging.

## Slide 42: Switches
Connect individual computers.

## Slide 43: Switches
Types: Two-layer (Cut-through), Three-layer (Routers).

## Slide 44: Switches
Store-and-forward vs. Cut-through switching.

## Slide 45: High-Speed LANs
Fast Ethernet (100 Mbps): IEEE 802.3u

## Slide 46: High-Speed LANs
Gigabit Ethernet (1 Gbps): IEEE 802.3ab, full-duplex and half-duplex modes, Jumbo frames.

## Slide 47: Wireless LANs (802.11)
Standards: 802.11a, 802.11b, 802.11g, 802.11n.

## Slide 48: Wireless LANs (802.11)
Modes: Infrastructure, Ad Hoc.

## Slide 49: Wireless LANs (802.11)
Physical Layer: Infrared, FHSS, DSSS, OFDM, HR-DSSS.

## Slide 50: Wireless LANs (802.11)
MAC Sublayer: CSMA/CA (Collision Avoidance), DCF (Distributed Coordination Function), PCF (Point Coordination Function).

## Slide 51: Bluetooth (802.15)
Wireless personal area network (PAN).

## Slide 52: Bluetooth (802.15)
Piconets (master and up to 7 active slaves), Scatternets.

## Slide 53: Bluetooth (802.15)
Protocol stack: Physical radio, Baseband, Link Manager, L2CAP, Audio/Control, Middleware, Applications.

## Slide 54: Data Link Layer Design Issues
Provides service interface to Network Layer (unacknowledged/acknowledged connectionless, acknowledged connection-oriented)

## Slide 55: Data Link Layer Design Issues
Handles transmission errors (checksums, ARQ)

## Slide 56: Data Link Layer Design Issues
Regulates data flow (stop-and-wait, sliding window flow control)

## Slide 57: Framing Methods
Byte Count (problem: error in count leads to desynchronization)

## Slide 58: Framing Methods
Flag Bytes with Byte Stuffing (inserts escape byte before 'accidental' flag bytes)

## Slide 59: Framing Methods
Flag Bits with Bit Stuffing (stuffs a 0 after five consecutive 1s in data)

## Slide 60: Framing Methods
Physical Layer Coding Violations (uses unused code combinations as delimiters)

## Slide 61: Error Control
Acknowledgement/Negative Acknowledgement (ACK/NAK)

## Slide 62: Error Control
Timers (detect lost frames)

## Slide 63: Error Control
Sequence Numbers (distinguish retransmissions from originals)

## Slide 64: Flow Control
Feedback-based (receiver informs sender)

## Slide 65: Flow Control
Rate-based (protocol limits sender's rate)

## Slide 66: Flow Control
Stop-and-Wait (one frame at a time, simple but slow)

## Slide 67: Flow Control
Sliding Window (multiple frames in flight, efficient but complex)

## Slide 68: Flow Control
Sliding Window types: Stop and Wait ARQ, Go-Back-N ARQ, Selective Repeat ARQ

## Slide 69: ARQ Techniques
Stop-and-Wait ARQ (simple, one frame at a time)

## Slide 70: ARQ Techniques
Go-Back-N ARQ (sender sends multiple frames, retransmits whole window if error)

## Slide 71: ARQ Techniques
Selective Repeat ARQ (sender retransmits only lost frames)

## Slide 72: Data Link Protocols: HDLC
Bit-oriented protocol

## Slide 73: Data Link Protocols: HDLC
Three station types: Primary, Secondary, Combined

## Slide 74: Data Link Protocols: HDLC
Frame types: Information (I), Supervisory (S), Unnumbered (U)

## Slide 75: Data Link Protocols: HDLC
Communication modes: Normal Response Mode (NRM), Asynchronous Balanced Mode (ABM)

## Slide 76: Data Link Protocols: PPP
Point-to-Point Protocol for internet

## Slide 77: Data Link Protocols: PPP
Provides framing, link control (LCP), network layer options (NCP)

## Slide 78: Data Link Protocols: PPP
Lacks flow control, simple error control, no addressing for multipoint

## Slide 79: Data Link Protocols: PPP
Phases: Dead, Establish, Authenticate, Network, Open, Terminate

## Slide 80: MAC Sublayer: IEEE 802
LLC (Logical Link Control): handles framing, flow, error control

## Slide 81: MAC Sublayer: IEEE 802
MAC (Media Access Control): access methods (CSMA/CD, Token Bus, Token Ring)

## Slide 82: MAC Sublayer: IEEE 802
IEEE 802.3 (Ethernet): CSMA/CD, various cabling types (10Base5, 10Base2, 10BaseT, 10BaseF)

## Slide 83: MAC Sublayer: IEEE 802
IEEE 802.4 (Token Bus): token passing on a bus topology

## Slide 84: MAC Sublayer: IEEE 802
IEEE 802.5 (Token Ring): token passing on a ring topology

## Slide 85: High-Speed LANs
Fast Ethernet (100 Mbps), Gigabit Ethernet (1 Gbps)

## Slide 86: High-Speed LANs
Full-duplex and half-duplex modes

## Slide 87: High-Speed LANs
Carrier extension, frame bursting, jumbo frames

## Slide 88: Wireless LANs: 802.11
Infrastructure mode (with access points)

## Slide 89: Wireless LANs: 802.11
Ad hoc mode (direct connection between devices)

## Slide 90: Wireless LANs: 802.11
Physical layer technologies: Infrared, FHSS, DSSS, OFDM

## Slide 91: Wireless LANs: 802.11
MAC sublayer: CSMA/CA (collision avoidance), DCF (distributed), PCF (point coordination)

## Slide 92: Wireless LANs: 802.11
Frame types: Data, Control, Management

## Slide 93: Wireless LANs: 802.11
Services: Distribution (association, disassociation, reassociation, distribution, integration), Station (authentication, deauthentication, privacy, data delivery)

## Slide 94: 802.15 (Bluetooth)
Wireless personal area network (PAN)

## Slide 95: 802.15 (Bluetooth)
Piconet (master and up to 7 active slaves)

## Slide 96: 802.15 (Bluetooth)
Scatternet (interconnected piconets)

## Slide 97: 802.15 (Bluetooth)
Link types: ACL (Asynchronous Connectionless), SCO (Synchronous Connection Oriented)

## Slide 98: 802.15 (Bluetooth)
Protocol stack: Physical, Baseband, Link Manager, L2CAP, Audio/Control, Middleware, Application